## Iptables Config File
iptables firewall is used to manage packet filtering and NAT rules. IPTables comes with all Linux distributions.
## Understanding Firewall
There are total 4 chains:
1. INPUT - The default chain is used for packets addressed to the system. Use this to open or close incoming ports (such as 80,25, and 110 etc) and ip addresses / subnet (such as 202.54.1.20/29).
2. OUTPUT - The default chain is used when packets are generating from the system. Use this open or close outgoing ports and ip addresses / subnets.
3. FORWARD - The default chains is used when packets send through another interface. Usually used when you setup Linux as router. For example, eth0 connected to ADSL/Cable modem and eth1 is connected to local LAN. Use FORWARD chain to send and receive traffic from LAN to the Internet.
4. RH-Firewall-1-INPUT - This is a user-defined custom chain. It is used by the INPUT, OUTPUT and FORWARD chains.
### Packet Matching Rules
1. Each packet starts at the first rule in the chain .
2. A packet proceeds until it matches a rule.
3. If a match found, then control will jump to the specified target (such as REJECT, ACCEPT, DROP).
### Target Meanings
1. The target ACCEPT means allow packet.
2. The target REJECT means to drop the packet and send an error message to remote host.
3. The target DROP means drop the packet and do not send an error message to remote host or sending host.
Type the following command to install iptables, enter:

# yum install iptables

## Turn On Firewall:
chkconfig iptables on
service iptables start

# restart the firewall
service iptables restart

# stop the firewall
service iptables stop
## Display Default Rules:
iptables -L

### Open Port:
To open port 80 (Http server) add the following before COMMIT line:
-A RH-Firewall-1-INPUT -m tcp -p tcp --dport 80 -j ACCEPT
To open port 53 (DNS Server) add the following before COMMIT line:
-A RH-Firewall-1-INPUT -m tcp -p tcp --dport 53 -j ACCEPT
-A RH-Firewall-1-INPUT -m udp -p tcp --dport 53 -j ACCEPT
To open port 443 (Https server) add the following before COMMIT line:
-A RH-Firewall-1-INPUT -m tcp -p tcp --dport 443 -j ACCEPT
To open port 25 (smtp server) add the following before COMMIT line:
-A RH-Firewall-1-INPUT -m tcp -p tcp --dport 25 -j ACCEPT

#### Only allow SSH traffic From 192.168.1.0/24 :
-A RH-Firewall-1-INPUT -s 192.168.1.0/24 -m state --state NEW -p tcp --dport 22 -j ACCEPT

#### Enable Printing Access For 192.168.1.0/24
-A RH-Firewall-1-INPUT -s 192.168.1.0/24 -m state --state NEW -p udp --dport 123 -j ACCEPT

#### Open FTP Port 21 (FTP):
-A RH-Firewall-1-INPUT -m state --state NEW -p tcp --dport 21 -j ACCEPT

### Log And Drop All Traffic:
Find the lines:
-A RH-Firewall-1-INPUT -j REJECT --reject-with icmp-host-prohibited
COMMIT
Update it as follows:
-A RH-Firewall-1-INPUT -j LOG
-A RH-Firewall-1-INPUT -j DROP
COMMIT
Save and close the file. Edit /etc/sysconfig/iptables-config, enter:

# vi /etc/sysconfig/iptables-config
# service iptables restart

Reference:
http://www.cyberciti.biz/faq/rhel-fedorta-linux-iptables-firewall-configuration-tutorial/
https://www.digitalocean.com/community/tutorials/how-to-set-up-a-firewall-using-iptables-on-ubuntu-14-04
http://www.thegeekstuff.com/2011/01/iptables-fundamentals/